## Slide 1: Voice Glider Plugin
(Phase Vocoder Implementation for the pitch shifting)
Presented by
Navaneeth Suresh Kumar
MS Music Engineering Student | Frost School of Music UM
Email : nss147@miami.edu
2022-2024 batch

## Slide 2: Introduction
Objectives
To build an audio FX plugin for vocal manipulation
Incorporating Phase vocoder algorithm for pitch shifting
Real-time vocal manipulation and effects.

## Slide 3: Problem Definition
There is not a lot of plugins to manipulate human voice and to design the unique sound that a producer needs
Musicians and sound designers require a dedicated tool for voice manipulation and voice enhancement, and make it interesting.
Why do I need to design this Audio Effect plugin?

## Slide 4: Solution
build a vocal processing plugin using juce framework. It needs to have functionalities to tweak the Saturation, modulate the amplitude, Pitch Shift and Gain parameters to add more variation to the sound.

## Slide 5: Major design Bocks of the plugin
Pitch Shifter : implemented the pitch shifter using phase vocoder and controls the pitch of the vocal
Saturation & bias: Adds character and grit to the vocal. Users can apply distortion to the audio, opening up possibilities for edgier and non-conventional timbres.
Amplitude Modulation(Tremolo): Amplitude modulation is a powerful tool for sculpting evolving and dynamic sounds. It allows users to introduce amplitude change over time, giving the audio an edge in creating expressive sounds.
Gain Control: Gain control is crucial for achieving the right balance in audio output. Musicians and sound designers can adjust the output level, ensuring it integrates seamlessly with other audio sources in their projects.

## Slide 6: Block Diagram
Input Audio
Applying Pitch Shift
Applying Distortion
Applying AM
Output Gain control
Sat
Rate
Depth
Juce Audio Buffer
Bias

## Slide 7: The phase vocoder performs time stretching and pitch scaling by transforming the audio into frequency domain.
The phase vocoder has an analysis section that performs an overlapped short-time FFT (ST-FFT) and a synthesis section that performs an overlapped inverse short-time FFT (IST-FFT). To time stretch a signal, the phase vocoder uses a larger hop size for the overlap-add operation in the synthesis section than the analysis section. Here, the hop size is the number of samples processed at one time.
As a result, there are more samples at the output than at the input although the frequency content remains the same. Now, you can pitch scale this signal by playing it back at a higher sample rate, which produces a signal with the original duration but a higher pitch.
Implementing Pitch Shifter using a Phase Vocoder approach
Notes: Analysis Section:
- Performs an Overlapped Short-Time Fast Fourier Transform (ST-FFT).
- Breaks down the audio signal into its frequency components over short time windows.
- Typically uses a smaller hop size for the analysis, which means it processes fewer samples at a time but with overlapping segments.
Synthesis Section:
- Performs an Overlapped Inverse Short-Time Fast Fourier Transform (IST-FFT).
- Reconstructs the audio signal from the modified frequency domain representation obtained during the analysis.
- Uses a larger hop size compared to the analysis section for the overlap-add operation.
- This larger hop size results in more samples at the output than at the input, preserving the frequency content but altering the duration of the signal.
Time Stretching:
- The phase vocoder's larger hop size during synthesis results in an output signal that has more samples than the original input but maintains the same frequency content.
- To perform time stretching, the synthesized signal with more samples can be played back at a higher sample rate without altering the frequency content.
- Increasing the sample rate while maintaining the original duration results in a signal with a higher pitch.
Pitch Scaling:
- By playing back the time-stretched signal at a higher sample rate, the duration remains the same as the original signal but with an increased pitch.
- Pitch scaling is achieved by altering the playback speed (sample rate) of the time-stretched signal while keeping the duration constant.

## Slide 8: Implementing Soft clipping saturation Using tanh()
2 * tanh(drive * input) / pi
Input
Output
Saturation
Drive

## Slide 9: Amplitude Modulation
Depth
input
m(n)
Frequency(Rate)
Carrier Signal
Sine Modulator
Output

## Slide 10: Feedbacks
User 1
Can be provided frequency shift as Semitones
Easy to use
Can include a output level indicator
User 2
Cool UI! Good design
Can be used for movies to create sound effects. (Especially for cartoon characters!)
Can be used for EDMs
User 3
Use FFT library for a better quality output
Good Design
Distortion is powerful. Can be lighter.

## Slide 11: Where I can use this plugin?
Music production : Electronic music and ambient music
To create cool vocal chops or vocal effects
Cartoons, Animations and films to manipulate the voice according to the character.
Sound Design and use to manipulate audio recording or voice recording
Live solo vocal performances
As a vocal enhancer for dubbing
Remixes
Chorus mixing and to create drops
Why should you Use this plugin?
This plugin gives you the freedom of designing the kind of character to a recording according to your application.
To design vocal chops of different tones according to the applications

## Slide 12: Thank You